## Slide 1: SpinalHDL
An alternative to standard HDL

## Slide 2: Summary
Language introduction
Language flow
Syntax introduction
Many examples

## Slide 3: Language introduction
Open source , started in december 2014
Focus on RTL description
Thinked to be interoperable with existing tools
  It generate VHDL/Verilog files
  It can integrate VHDL/Verilog IP as blackbox
Abstraction level :
  You can design things similary to VHDL/Verilog
  If you want to, you can use many abstraction utils and also define new ones

## Slide 4: Language flow
Describe your RTL
Generate the VHDL/Verilog
Simulate and synthesize

## Slide 5: Some points about Spinal
There is no logic overhead in the generated code. (I swear !)
Spinal HDL is a RTL language. But the generated VHDL/Verilog is simulatable with all standards EDA tools.
The component hierarchy and all names are preserved during the VHDL/Verilog generation.

## Slide 6: A simple component
class MyComponent extends Component { val io = new Bundle { val a = in Bool val result = out Bool } io.result := io.a }
Notes: It’s scala, but with some pretty things (in Bool in this case)
New Bundle is the definition of a new datatype, a little bit like records in VHDL or struct in Verilog, but with individual element direction specification
This code wire io.a to io.output

## Slide 7: Combinatorial logic
class MyComponent extends Component { val io = new Bundle { val a = in Bool val b = in Bool val c = in Bool val result = out Bool } io.result := (io.a & io.b) | (!io.c) }
Notes: Like in VHDL you can do combinatorial things.
Anyway you can read the value each out signal, like a VHDL buffer.

## Slide 8: Signals
class MyComponent extends Component { val io = new Bundle { val a = in Bool val b = in Bool val c = in Bool val result = out Bool } val a_and_b = Bool
a_and_b := io.a & io.b
val not_c = ! io.c
io.result := a_and_b | not_c }
Notes: Declare what you need where you need and directly affect the value that you want (not_c signal).
For example if you don’t assigne a_and_b to any value, spinalHDL tell you.

## Slide 9: Generated VHDL
class MyComponent extends Component { val io = new Bundle { val a = in Bool val b = in Bool val c = in Bool val result = out Bool } val a_and_b = io.a & io.b val not_c = !io.c io.result := a_and_b | not_c }
entity MyComponent is port( io_a : in std_logic; io_b : in std_logic; io_c : in std_logic; io_result : out std_logic ); end MyComponent; architecture arch of MyComponent is signal a_and_b : std_logic; signal not_c : std_logic; begin io_result <= (a_and_b or not_c); a_and_b <= (io_a and io_b); not_c <= (not io_c); end arch;
Notes: As you can see you can avoid the split between the signal declaration and the signal logic.

## Slide 10: Registers
class MyComponent extends Component { val io = new Bundle { val a = in Bool } val reg1 = Reg(Bool)
val reg2 = Reg(Bool) init (False)
val reg3 = Reg(Bool) reg3 := ! io.a }
Notes: You don’t need for each register to specify his clock, it’s implicit (next clock)
There is no process !
Reg1 is a simple register with no reset
Reg2 is a register with a reset value at false
Reg3 is the same than Reg2 with a more compact syntax
Reg4 is a register that take the io.a value at each clock. You can add the init(XXX) to specify a reset value.

## Slide 11: No more Process/Always blocks
val cond = Bool val mySignal = Bool val myRegister = Reg(UInt(4 bits)) val myRegisterWithReset = Reg(UInt(4 bits)) init (0) mySignal := False when(cond) { mySignal := True myRegister := myRegister + 1 myRegisterWithReset := myRegisterWithReset + 1 }
Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset

## Slide 12: Component internal organisation
class TopLevel extends Component {
//… val logicArea = new Area { val flag = Bool }
val fsmArea = new Area { when(logicArea.flag) {
//…
} } }
Notes: There is the concept of Area, that allow you to define some sub part into a component. That help you to keep a good structure.
You can use the switch statement to.

## Slide 13: Component instance
class SubComponent extends Component{ val io = new Bundle { val input = in Bool val result = out Bool } ... } class TopLevel extends Component { val io = new Bundle { val a = in Bool val b = in Bool val result = out Bool } val sub = new SubComponent sub.io.input := io.a io.result := sub.io.result | io.b }
Notes: No declaration of components instances io. You directly wire it with «componentInstance.io.XXX»

## Slide 14: UInt, Vec, When
class MyComponent extends Component { val io = new Bundle { val conds = in Vec(Bool,2) val result = out UInt(4 bits) } when(io.conds(0)){ io.result := 2 when(io.conds(1)){ io.result := 1 } } otherwise { io.result := 0 } }
Notes: You can define a array of data elements by using Vec(numberOfElement,dataType)
For hardware conditional blocks, you can use the when(cond){}.elsewhen(cond){}.otherwise {} The dot before the elsewhen is mandatory, but not for the otherwise. It’s because of scala.
N.B. En each when, you can mix assignement of syncronous and asyncronous logic. You don’t have the VHDL process barrier

## Slide 15: Enum, Switch
object MyEnum extends SpinalEnum { val state0, state1 = newElement() } class MyComponent extends Component { val state = Reg(MyEnum) init(MyEnum.state0)
switch(state) { is(MyEnum.state0) { } is(MyEnum.state1) { } default{ } } }
Notes: There is the concept of Area, that allow you to define some sub part into a component. That help you to keep a good structure.
You can use the switch statement to.

## Slide 16: For, Variable, Generics
class CarryAdder(size: Int) extends Component { val io = new Bundle { val a = in UInt (size bits) val b = in UInt (size bits) val result = out UInt (size bits) } var c = False for (i <- 0 until size) { val x = io.a(i) val y = io.b(i) io.result(i) := x ^ y ^ c c \= (x & y) | (x & c) | (y & c); } }
Notes: This component has a construction parameter (size). It’s like generics in VHDL.
The carry adder use a carry variable (c) . Variable in spinal play with scala var.
If you totaly override the value of the variable, you can use the = assignement.
If you do a incremental assignement, (for example a conditional (when) assignement), you must use the \= assignement operator.
You can declare intermediate value (a,b) in the for. It’s as you want.

## Slide 17: Latch/Loop
class MyComponent extends Component { val io = new Bundle { val a = in Bool val result = out Bool }
//Latch/Loop detected => Error message will come from Spinal
io.result := io.a | io.result }
Notes: Spinal check if there is combinatorial loop and print a error when one is detected.

## Slide 18: ClockDomains
class MyTopLevel extends Component { val io = new Bundle { val coreClk = in Bool val coreReset = in Bool }
val coreClockDomain = ClockDomain( clock = io.coreClk, reset = io.coreReset, config = ClockDomainConfig( clockEdge = RISING, resetKind = ASYNC, resetActiveLevel = HIGH ) ) val coreArea = new ClockingArea(coreClockDomain) { val myCoreClockedRegister = Reg(UInt(4 bit)) //... } }

## Slide 19: Memory
//Memory of 1024 Bool val syncRam = Mem(Bool, 1024) val asyncRam = Mem(Bool, 1024) //Write them syncRam(5) := True asyncRam(5) := True //Read them val syncRam = mem.readSync(6) val asyncRam = mem.readAsync(4)

## Slide 20: Function
// Input RGB color val r,g,b = UInt(8 bits) // Define a function to multiply a UInt by a scala Float value. def coefMul(value : UInt,by : Float) : UInt = (value * U((255*by).toInt,8 bits) >> 8) //Calculate the gray level val gray = coefMul(r, 0.3f) + coefMul(g, 0.4f) + coefMul(b, 0.3f)
Notes: In VHDL you can’t create a function that assign combinatoral and sequancial logic

## Slide 21: Function, User utils (1)
case class Color(channelWidth: Int) extends Bundle { val r = UInt(channelWidth bit) val g = UInt(channelWidth bit) val b = UInt(channelWidth bit) def +(that: Color): Color = { val result = Color(channelWidth)
result.r := this.r + that.r result.g := this.g + that.g result.b := this.b + that.b return result } }
Notes: You can extend a bundle definition with all user function that you want. Here is a example where the plus operator is provided for Color Bundle(with overflow protection).
You can define inner function (channelAdd)
AdderAndCarry return 2 things, the sum of 2 Uint and the carry value. (scala allow return mutiple value in the same type by using Tuple)

## Slide 22: Function, User utils (2)
class ColorSumming(sourceCount: Int, channelWidth: Int) extends Component { val io = new Bundle { val sources = in Vec(Color(channelWidth), sourceCount) val result = out(Color(channelWidth)) } var sum = io.sources(0) for (i <- 1 until sourceCount) { sum \= sum + io.sources(i) } io.result := sum }
Notes: Here is a example of a block with N Color input, and a result output that is the sum of all colors by using the precedent slide plus operator.

## Slide 23: Basic abstractions
val timeout = Timeout(1000) when(timeout){ //implicit conversion to Bool timeout.clear() //Clear the flag and the internal counter } //Create a counter of 10 states (0 to 9) val counter = Counter(10) counter.clear() //When called it reset the counter. It's not a flag counter.increment() //When called it increment the counter. It's not a flag counter.value //current value counter.valueNext //Next value counter.willOverflow //Flag that indicate if the counter overflow this cycle when(counter === 5){ …}
Notes: Some basics abstraction are defined in the Spinal Lib.

## Slide 24: Flow, Stream
case class Flow[T <: Data](payloadType: T) extends Bundle { val valid = Bool val payload : T = Flow(payloadType) } case class Stream[T <: Data](payloadType: T) extends Bundle { val valid = Bool val ready = Bool val payload : T = Stream(payloadType) }
val myStreamOfRGB= Stream(RGB(8,8,8))

## Slide 25: Stream components
class Fifo[T <: Data](payloadType: T, depth: Int) extends Component { val io = new Bundle { val push = slave Stream (payloadType) val pop = master Stream (payloadType) }
//… } class Arbiter[T <: Data](payloadType: T, portCount: Int) extends Component { val io = new Bundle { val sources = Vec(slave(Stream(payloadType)), portCount) val sink = master(Stream(payloadType)) } //... }

## Slide 26: Stream functions
case class Stream[T <: Data](payloadType: T) extends Bundle { // ... def connectFrom(that: Stream[T]) = { // some connections between this and that } def stage(): Stream[T] = { val outputStage = Stream(dataType) val validReg = RegInit(False) val payloadReg = Reg(payloadType) // some logic return outputStage } def << (that: Stream[T]) = this.connectFrom(that) def <-< (that: Stream[T]) = this << that.stage() } val myStreamA,myStreamB = Stream(UInt(8 bits)) myStreamA <-< myStreamB
Notes: In system verilog, even if you can define interface, you can’t define function/task inside it that will generate flops and logic.
This is a breaking point with systemverilog, some application of that will come in next slides

## Slide 27: Functional programming
val addresses = Vec(UInt(8 bits),4) val key = UInt(8 bits) val hits = addresses.map(address => address === key) val hit = hits.reduce((a,b) => a || b)

## Slide 28: Scala is here to help you
class SinusGenerator(resolutionWidth : Int,sampleCount : Int) extends Component { val io = new Bundle { val sin = out SInt (resolutionWidth bits) } def sinTable = (0 until sampleCount).map(sampleIndex => { val sinValue = Math.sin(2 * Math.PI * sampleIndex / sampleCount) S((sinValue * ((1 << resolutionWidth) / 2 - 1)).toInt, resolutionWidth bits) }) val rom = Mem(SInt(resolutionWidth bits), initialContent = sinTable) val phase = CounterFreeRun(sampleCount) io.sin := rom.readSync(phase) }

## Slide 29: Netlist analyser / Latency analysis
class MyComponentWithLatencyAssert extends Component { val io = new Bundle { val slavePort = slave Stream (UInt(8 bits)) val masterPort = master Stream (UInt(8 bits)) } //These 3 line are equivalent to io.slavePort.queue(16) >/-> io.masterPort val fifo = new StreamFifo((UInt(8 bits)),16) fifo.io.push << io.slavePort // << is a connection operator without decoupling fifo.io.pop >/-> io.masterPort //>/-> is a connection operator with decoupling assert(3 == latencyAnalysis(io.slavePort.payload,io.masterPort.payload)) assert(2 == latencyAnalysis(io.masterPort.ready,io.slavePort.ready)) }
Notes: Because spinal build a netlist in the memory, you can use it to extract some information, for example latency (in cycle) between some points of you design.
To do that, call LatencyAnalysis and give to it as argument some the start point, some check point and the end point of you path. It look for the shortest path and return how many cycle there is.

## Slide 30: FSM
They could be defined with regular syntax (Enum,Switch)
You can also use a much more friendly syntax, fully integrated, with following features :
  onEntry / onExit / whenIsActive / whenIsNext blocs
  State with inner FSM
  State with multiple inner FSM (parallel execution)
  Delay state
  You can extends the syntax by defining new state types

## Slide 31: FSM style A
val fsm = new StateMachine{ io.result := False val counter = Reg(UInt(8 bits)) init (0)
val stateA : State = new State with EntryPoint{ whenIsActive (goto(stateB)) }
val stateB : State = new State{ onEntry(counter := 0) whenIsActive { counter := counter + 1 when(counter === 4){ goto(stateC) } } onExit(io.result := True) }
val stateC : State = new State{ whenIsActive (goto(stateA)) } }
val io = new Bundle{ val result = out Bool }

## Slide 32: FSM style B
val io = new Bundle{ val result = out Bool }
val fsm = new StateMachine{ val stateA = new State with EntryPoint val stateB = new State val stateC = new State val counter = Reg(UInt(8 bits)) init (0) io.result := False stateA .whenIsActive (goto(stateB)) stateB .onEntry(counter := 0) .whenIsActive { counter := counter + 1 when(counter === 4){ goto(stateC) } } .onExit(io.result := True) stateC .whenIsActive (goto(stateA)) }

## Slide 33: Meta-hardware description

## Slide 34
Name | Type | Access | Address | Description
clockDivider | UInt | RW | 0 | Set the UartCtrl clock divider
frame | UartCtrlFrameConfig | RW | 4 | Set the dataLength, the parity and the stop bit configuration
writeCmd | Bits | W | 8 | Send a write command to the UartCtrl
writeBusy | Bool | R | 8 | Bit 0 => zero when a new writeCmd could be sent
read | Bool / Bits | R | 12 | Bit 7 downto 0 => fifo pop payload Bit 31 => fifo pop valid

## Slide 35
class AvalonUartCtrl(uartCtrlConfig : UartCtrlGenerics, rxFifoDepth : Int) extends Component{ val io = new Bundle{ val bus = slave(AvalonMM(…)) val uart = master(Uart()) } val uartCtrl = new UartCtrl(uartCtrlConfig) io.uart <> uartCtrl.io.uart val busCtrl = AvalonMMSlaveFactory(io.bus)
//Make clockDivider register busCtrl.driveAndRead(uartCtrl.io.config.clockDivider, address = 0)
//Make frame register busCtrl.driveAndRead(uartCtrl.io.config.frame, address = 4)
//Make writeCmd register val writeFlow = busCtrl.createAndDriveFlow(Bits(uartCtrlConfig.dataWidthMax bits), address = 8) writeFlow.toStream.stage() >> uartCtrl.io.write
//Make writeBusy register busCtrl.read(uartCtrl.io.write.valid, address = 8)
//Make read register busCtrl.readStreamNonBlocking(uartCtrl.io.read.toStream.queue(rxFifoDepth),
address = 12,validBitOffset = 31,payloadBitOffset = 0) }

## Slide 36: About FSM and AvalonMMSlaveFactory
Both aren’t part of Spinal core but are implemented on the top of it in the Spinal lib. Which mean these tools were created without any special interaction or special knowledge of the Spinal compiler.
They are only a mix of Scala OOP/FP with some Spinal basic syntax to generate the right hardware !

## Slide 37: About Scala
Free Scala IDE (eclipse, intelij)
  Highlight syntax error
  Renaming flexibility
  Intelligent auto completion
  Code’s structure overview
  Navigation tools
Allow you to extend the language
Provide many libraries

## Slide 38: Spinal work perfectly on FPGA
RISCV CPU, 5 stages, 1.15 DMIPS/Mhz
  MUL/DIV
  Instruction/Data cache
  Interrupts
  JTAG debugging
Avalon/APB UART
Avalon VGA
Pipelined and multi-core fractal accelerator

## Slide 39: About Spinal project
Completely open source :
    https://github.com/SpinalHDL/SpinalHDL
Online documentation :
    https://spinalhdl.github.io/SpinalDoc/
Ready to use base project :
    https://github.com/SpinalHDL/SpinalBaseProject
Communication channels :
    spinalhdl@gmail.com
    https://gitter.im/SpinalHDL/SpinalHDL
    https://github.com/SpinalHDL/SpinalHDL/issues