## Slide 1: Spinal HDL
An alternative to standard HDL

## Slide 2: Summary
Why a new language
Language introduction / dissection
Examples

## Slide 3: Why a new language
Because of current HDL
  Verbosity, endless wiring, copy past
  Wire level, can’t define abstractions
  Broken features
    Can’t parameterize records
    Can’t define record’s elements directions individually
    SystemVerilog interface parameterized datatype
  They were initially designed for simulation
  Heavy legacy

## Slide 4: Language introduction
Open Source , started in december 2014
Is designed for RTL
Compatibility is assured
  It generate a VHDL file
  It can integrate VHDL IP as blackbox
Abstraction level :
  Start at the same level than VHDL
  Finish between VHDL and HLS
  The user can create new levels

## Slide 5: Language dissection
SpinalHDL is a «Scala internal DSL»
  You can use all Scala syntax / library
  Scala IDE are mature and free
  Object oriented and functional paradigms
How it work
  Use the library => it build internal netlist => VHDL
2 layers
  Core (low level RTL)
  Lib (high level RTL, based on Code layer)

## Slide 6: A simple component
class MyComponent extends Component { val io = new Bundle { val a = in Bool val output = out Bool } io.output := io.a }
Notes: It’s scala, but with some pretty things (in Bool in this case)
New Bundle is the definition of a new datatype, a little bit like records in VHDL or struct in Verilog, but with individual element direction specification
This code wire io.a to io.output

## Slide 7: Combinatorial, Latch/Loop
class MyComponent extends Component { val io = new Bundle { val a = in Bool val b = in Bool val c = out Bool val output = out Bool } io.output := (io.a & io.b) | (!io.c) }
class MyComponent extends Component { //… io.output := io.a | io.output //Latch/Loop detected, not allowed }
Notes: Like in VHDL you can do combinatorial things.
Spinal check if there is combinatorial loop and print a error when one is detected.
Anyway you can read the value each out signal, like a VHDL buffer.

## Slide 8: Signals
class MyComponent extends Component { val io = new Bundle { val a = in Bool val b = in Bool val c = in Bool val output = out Bool } val a_and_b = Bool
a_and_b := io.a & io.b val not_c = !io.c io.output := a_and_b | not_c }
Notes: Declare what you need where you need and directly affect the value that you want (not_c signal).
For example if you don’t assigne a_and_b to any value, spinalHDL tell you.

## Slide 9: Generated VHDL
class MyComponent extends Component { val io = new Bundle { val a = in Bool val b = in Bool val c = in Bool val output = out Bool } val a_and_b = io.a & io.b val not_c = !io.c io.output := a_and_b | not_c }
library ieee; use ieee.std_logic_1164.all; use ieee.numeric_std.all;
entity MyComponent is port( io_a : in std_logic; io_b : in std_logic; io_c : in std_logic; io_output : out std_logic ); end MyComponent; architecture arch of MyComponent is signal a_and_b : std_logic; signal not_c : std_logic; begin io_output <= (a_and_b or not_c); a_and_b <= (io_a and io_b); not_c <= (not io_c); end arch;
Notes: As you can see you can avoid the split between the signal declaration and the signal logic.

## Slide 10: Registers
class MyComponent extends Component { val io = new Bundle { val a = in Bool } val reg1 = Reg(Bool) val reg2 = Reg(Bool) init(False) val reg3 = RegInit(False) val reg4 = RegNext(io.a) }
Notes: You don’t need for each register to specify his clock, it’s implicit (next clock)
There is no process !
Reg1 is a simple register with no reset
Reg2 is a register with a reset value at false
Reg3 is the same than Reg2 with a more compact syntax
Reg4 is a register that take the io.a value at each clock. You can add the init(XXX) to specify a reset value.

## Slide 11: ClockDomains, Area
class MyTopLevel extends Component { val io = new Bundle { val coreClk = in Bool val coreReset = in Bool val peripheralClk = in Bool val peripheralReset = in Bool } val coreClockDomain = ClockDomain(io.coreClk, io.coreReset) val peripheralClockDomain = ClockDomain(io.peripheralClk, io.peripheralReset) val coreArea = new ClockingArea(coreClockDomain){ val myCoreClockedRegister = Reg(UInt(4 bit)) } val peripheralArea = new ClockingArea(peripheralClockDomain){ val myPeripheralClockedRegister = Reg(UInt(4 bit)) myPeripheralClockedRegister := coreArea.myCoreClockedRegister //Not allowed myPeripheralClockedRegister := BufferCC(coreArea.myCoreClockedRegister) } }
Notes: In this example, there is 2 ClockDomain created by using input signals.
Then 2 ClockingArea are created. Each ClockingArea has a specified ClockDomain. All register inside use this specified ClockDomain (implicit).
myPeripheralClockedRegister := coreArea.myCoreClockedRegister is not allowed because it cross ClockDomain (safe). You must add a special tag to myPeripheralClockedRegister or use the BufferCC function that add 2 register (default) syncronisation stages.

## Slide 12: Component instance
class MySubComponent extends Component{ val io = new Bundle { val subIn = in Bool val subOut = out Bool } ... } class MyComponent extends Component { val io = new Bundle { val a = in Bool val b = in Bool val output = out Bool } val compInstance = new MySubComponent compInstance.io.subIn := io.a io.output := compInstance.io.subOut | io.b }
Notes: No declaration of components instances io. You directly wire it with «componentInstance.io.XXX»

## Slide 13: Uint, Vec, When
class MyComponent extends Component { val io = new Bundle { val conds = in Vec(2,Bool) val output = out UInt(4 bit) } when(io.conds(0)){ io.output := 2 when(io.conds(1)){ io.output := 1 } } otherwise { io.output := 0 } }
Notes: You can define a array of data elements by using Vec(numberOfElement,dataType)
For hardware conditional blocks, you can use the when(cond){}.elsewhen(cond){}.otherwise {} The dot before the elsewhen is mandatory, but not for the otherwise. It’s because of scala.
N.B. En each when, you can mix assignement of syncronous and asyncronous logic. You don’t have the VHDL process barrier

## Slide 14: Enum, Area, switch
object MyEnum extends SpinalEnum { val state0, state1, anotherState = Value } abstract class MyComponent extends Component { val logicOfA = new Area { val flag = Bool val logic = Bool } val fsm = new Area { import MyEnum._ val state = Reg(MyEnum()) init (state0) switch(state) { is(state0) { when(logicOfA.flag) { state := state1 } } default { } } } }
Notes: I agree that the SpinalEnum syntax is not the best. Probable this syntax is subject to change (not the concept).
There is the concept of Area, that allow you to define some sub part into a component. That help you to keep a good structure.
You can use the switch statement to.

## Slide 15: For, Variable, Generics
class CarryAdder(size: Int) extends Component { val io = new Bundle { val a = in UInt (size bit) val b = in UInt (size bit) val result = out UInt (size bit) } var c = False for (i <- 0 until size) { val a = io.a(i) val b = io.b(i) io.result(i) := a ^ b ^ c c = (a & b) | (a & c) | (b & c); } }
Notes: This component has a construction parameter (size). It’s like generics in VHDL.
The carry adder use a carry variable (c) . Variable in spinal play with scala var.
If you totaly override the value of the variable, you can use the = assignement.
If you do a incremental assignement, (for example a conditional (when) assignement), you must use the \= assignement operator.
You can declare intermediate value (a,b) in the for. It’s as you want.

## Slide 16: Bundle, Generics, Vec, Packing
case class Color(channelWidth : Int) extends Bundle{ val r = UInt(channelWidth bit) val g = UInt(channelWidth bit) val b = UInt(channelWidth bit) } class MyColorSelector(sourceCount : Int,channelWidth: Int) extends Component { val io = new Bundle { val sel = in UInt(log2Up(sourceCount) bit) val sources = in Vec(sourceCount,Color(channelWidth)) val result = out Bits (3*channelWidth bit) } val selectedSource = io.sources(io.sel) io.result := toBits(selectedSource) }
Notes: You can define parametrized (or not) data structure by using the Bundle class. Then you can use it where you want, even in component IO !
Sources is a parametrized vector on a paremetrized data structure in a IO definition. In VHDL you can’t.
There is a builtin log2Up function to give how many bit you need to encode a given number of state.
You can pack a data structure into a Bits value, just use the toBits function. (you can unpack to by using «assignFromBits» function)

## Slide 17: Function, User utils (1)
case class Color(channelWidth: Int) extends Bundle { val r = UInt(channelWidth bit) val g = UInt(channelWidth bit) val b = UInt(channelWidth bit) def +(that: Color): Color = { assert(that.channelWidth == this.channelWidth) val result = cloneOf(this) result.r := channelAdd(this.r, that.r) result.g := channelAdd(this.g, that.g) result.b := channelAdd(this.b, that.b) def channelAdd(left: UInt, right: UInt): UInt = { val (value, carry) = adderAndCarry(right, left) return Mux(carry, left.maxValue, value) } return result } }
Notes: You can extend a bundle definition with all user function that you want. Here is a example where the plus operator is provided for Color Bundle(with overflow protection).
You can define inner function (channelAdd)
AdderAndCarry return 2 things, the sum of 2 Uint and the carry value. (scala allow return mutiple value in the same type by using Tuple)

## Slide 18: Function, User utils (2)
class MyColorSumming(sourceCount: Int, channelWidth: Int) extends Component { val io = new Bundle { val sources = in Vec(sourceCount, Color(channelWidth)) val result = out(Color(channelWidth)) } var sum = io.sources(0) for (i <- 1 until sourceCount) { sum = sum + io.sources(i) } io.result := sum // But you can do all this stuff by this way, balanced is bonus : // io.result := io.sources.reduceBalancedSpinal(_ + _) }
Notes: Here is a example of a block with N Color input, and a result output that is the sum of all colors by using the precedent slide plus operator.

## Slide 19: Flow, Handshake, Fragment
case class Flow[T <: Data](dataType: T) extends Bundle { val valid = Bool val data: T = cloneOf(dataType) //.. } case class Handshake[T <: Data](dataType: T) extends Bundle { val valid = Bool val ready = Bool val data: T = cloneOf(dataType) //.. } case class Fragment[T <: Data](dataType: T) extends Bundle { val last = Bool val data: T = cloneOf(dataType) //.. }
Notes: The spinal lib define 3 basics bus for a general usage : Flow, Handshake, Fragment. Handshake is like each channel of one AXI bus.
Fragment is not really a bus, it’s the concept that you have a big packet of data, and you need to serialize it into multiple fragment. For example a VGA frame buffer where each pixel are one Fragment, or for example a configuration register of 32 bits can be represented by using 4 fragment of 8 bits. You create a «Flow of Fragment of a given dataType» or a «Handshake of Fragment of a given dataType».

## Slide 20: Handshake examples
class HandshakeFifo[T <: Data](dataType: T, depth: Int) extends Component{ val io = new Bundle { val pushPort = slave Handshake (dataType) val popPort = master Handshake (dataType) val occupancy = out UInt (log2Up(depth + 1) bit) } //... } class HandshakeArbiter[T <: Data](dataType: T, portCount: Int) extends Component{ val io = new Bundle { val inputs = Vec(portCount, slave Handshake (dataType)) val output = master Handshake (dataType) val chosen = out UInt (log2Up(portCount) bit) } //... } class HandshakeFork[T <: Data](dataType: T, portCount: Int) extends Component{ val io = new Bundle { val input = slave Handshake (dataType) val output = Vec(portCount, master Handshake (dataType)) } //... }
Notes: There is some exemple general component that using Handshake

## Slide 21: Handshake functions
val cond = Bool val inPort = Handshake(Bits(32 bit)) val outPort = Handshake(Bits(32 bit)) outPort << inPort outPort <-< inPort outPort </< inPort outPort <-/< inPort val haltedPort = inPort.haltWhen(cond) // & operator val filteredPort = inPort.throwWhen(inPort.data === 0) val outPortWithMsb = inPort.translateWith(inPort.data.msb) // ~ operator
Notes: By using Handshake, some utils are free.
<< is a direct connection
<-< is a connection with flipflop that cut master to slave data path (pipelining)
</< is a connection with flipflop that cut slave to master data path (pipelining)
<-/< is a connection with flipflip that cut all path between the master and the slave (pipelining)

## Slide 22: Flow of Fragment example
case class LogicAnalyserConfig() extends Bundle{ val trigger = new Bundle{ val delay = UInt(32 bit) //... } val logger = new Bundle{ val samplesLeftAfterTrigger = UInt(8 bit) //... } } class LogicAnalyser extends Component { val io = new Bundle { val cfgPort = slave Flow Fragment(Bits(8 bit)) } val waitTrigger = io.cfgPort filterHeader (0x01) toRegOf (Bool) init (False) val userTrigger = io.cfgPort pulseOn (0x02) val configs = io.cfgPort filterHeader (0x0F) toRegOf(LogicAnalyserConfig()) }
Notes: Here is the example of a hardware logic analyser implementation.
LogicAnalyserConfig define all configs of this logic analyser.
By using the cfgPort, all internal register created/loaded.
filterHeader look the first fragment of each packet. If the value doesn’t match with the parameter, the rest of the packet is not transmited behind
toRegOf translate a packet of Bits into a register of the given dataType
pulseOn emit a one clock pulse if the first fragment of one packet match with the argument

## Slide 23: Generator, Logic Analyser
val logicAnalyser = LogicAnalyserBuilder() .setSampleCount(256) .exTrigger(somewhere.inThe.hierarchy.trigger) .probe(somewhere.inThe.hierarchy.signalA) .probe(somewhere.inThe.hierarchy.signalB) .probe(somewhere.signalC) .build val uartCtrl = new UartCtrl() uartCtrl.read >> logicAnalyser.io.slavePort uartCtrl.write << logicAnalyser.io.masterPort
Notes: In spinal there is a library that provide a hardware logic analyser, like SignalTape II from Altera.
To create one, you can use the LogicAnalyserBuilder, give all your wish and the call build function. It’s a «builder pattern».
As you can see, you can give signals that are somewhere into the hierarchy, Spinal provide the possibility to «pull» each signal throug the design. It’ could be usefull for FPGA design in the developpment phase.

## Slide 24: Netlist analyer / Latency analysis
class MyComponentWithLatencyAssert extends Component { val io = new Bundle { val slavePort = slave Handshake (UInt(8 bit)) val masterPort = master Handshake (UInt(8 bit)) } //These 3 line are equivalent to io.slavePort.queue(16) >/-> io.masterPort val fifo = new HandshakeFifo((UInt(8 bit)),16) fifo.io.push << io.slavePort fifo.io.pop >/-> io.masterPort assert(3 == latencyAnalysis(io.slavePort.data,io.masterPort.data)) assert(2 == latencyAnalysis(io.masterPort.ready,io.slavePort.ready)) }
Notes: Because spinal build a netlist in the memory, you can use it to extract some information, for example latency (in cycle) between some points of you design.
To do that, call LatencyAnalysis and give to it as argument some the start point, some check point and the end point of you path. It look for the shortest path and return how many cycle there is.

## Slide 25: ?